2700PR SERIES MANUAL

Manual valve(s) shall be 2700 PR Series 3/4" or 1" models as manufactured under the brand name of Irritrol or approved equal. Valve shall meet ASSE, IAPMO, CSA and City of Los Angeles standards.

Construction: Valve body shall be constructed of corrosion- and UV-resistant PVC material. Valve shall have a convenient manual control handle and a non-rotating Buna-N shut-off seal for longer life. Valve shall have contamination guard to protect valve stem threads.

Operation: Valve shall have a working pressure range from 10 psi minimum to 150 psi maximum and a flow range from .25 GPM to 30 GPM.